## Slide 1
FTire and Puzzling Tire Physics:
Teacher, not Student
Michael Gipser
Esslingen University of Applied Sciences
& cosin scientific software
Notes: Contents
Modelization: Range of Application
Modelization: Model Family (2)
Modelization: Features
Modelization: Input and Output Signals (2)
Modelization: Operating Conditions
Modelization: Passenger Car Tire Design
Modelization: Parts of the Model
Modelization: Belt Segments (2)
Modelization: In-Plane Bending
Modelization: Out-of-Plane Bending
Modelization: Lateral Bending
Modelization: Belt Torsion & Twist
Modelization: Dynamic Radial Stiffness (2)
Modelization: Hysteresis Model
Modelization: Inflation Pressure (2)
Modelization: Rim-to-Belt Contact
Modelization: Newmark Integation
Modelization: Road Contact
Modelization: Road Contact Equations (5)
Modelization: Friction Element Dynamics
Modelization: Example (Side-slip Sweep)
Modelization: Tread Pattern
Modelization: Thermal Model (3)
Modelization: Wear Model (2)
Model Data
Model Data: Static Properties
Model Data: Modal Properties (2)
Model Data: Tread Data
Model Data: Additional Data
Model Data: Preprocessing (4)
Computing Time
Criteria for Choice of Measurements
Approaches for Parameterization
FTire/fit GUI
FTire/fit Features
FTire/fit De-Coupling of Identification Process
FTire/fit Results: Cleat Tests (4)
FTire/calc GUI
FTire/calc Features
FTire/calc FETire
FTire/calc Input Data (2)
FTire/calc Tire Layer Structure Template
FTire/calc Cross Section Geometry
FTire/calc Tread Pattern
FTire/calc Visualization (2)
FTire/estim Qualified Data Estimation
FTire/estim Independent Variables
FTire/estim Data to be Estimated
FTire/estim Example
FTire/estim Formulae Customization Mask
FTire/tools
FTire/tools Static Analysis
FTire/tools Modal Analysis
FTire/tools Linearization (2)
FTire/tools Steady-State Analysis
FTire/tools 'Show Info’
FTire/tools More Tools..
FTire/sim
FTire/sim Example (4)
FTire/sim Results: Handling (6)
FTire/link
Interface to Road Models
Regular Grid Road
User-Defined Road Model (URM)

## Slide 2: FTire and Puzzling Tire Physics: Teacher, not Student
Why is FTire a teacher?
What can FTire teach?
How does FTire teach?

## Slide 3: FTire and Puzzling Tire Physics: Teacher, not Student
Why is FTire a teacher?
What can FTire teach?
How does FTire teach?

## Slide 4
Complexity & Potential Application Range
MF-Tyre
Magic Formula
Tyre Model
in Different Versions
TMeasy
Tyre Model 'Easy-To-Use'
TameTire
Thermo-Mechanical
Slip-Based
Steady-State
Tire Model (Michelin)
MF-Swift
Short Wavelength
Intermediate Frequency
Tire Model
The World of Tire Models
CDTire
Comfort
and Durability
Tire Model
Explicit FE
Models
Abaqus,..
RMOD-K 7
Reifenmodell
Komfort
FTire
Flexible
Structure
Tire Model

## Slide 5
MF-Tyre
Magic Formula
Tyre Model
in Different Versions
TMeasy
Tyre Model 'Easy-To-Use'
TameTire
Thermo-Mechanical
Slip-Based
Steady-State
Tire Model (Michelin)
MF-Swift
Short Wavelength
Intermediate Frequency
Tire Model
The Descriptive Approach
the descriptive approach: ‘focus on effect rather than on cause’
mathematical quantitative description of most important but isolated properties
combination by assumed superposition of nonlinear properties with nonlinear cross-correlation

## Slide 6
MF-Tyre
Magic Formula
Tyre Model
in Different Versions
TMeasy
Tyre Model 'Easy-To-Use'
TameTire
Thermo-Mechanical
Slip-Based
Steady-State
Tire Model (Michelin)
MF-Swift
Short Wavelength
Intermediate Frequency
Tire Model
The Descriptive Approach
Tire model is student;
the developer must teach his model its complete behavior
‘you get what you have programmed’

## Slide 7
The Descriptive Approach
pure slip, single wheel load
combined slip
stand still, parking
curved drum surface
pure slip, Fz-dependent
pure handling with full vehicle model?
simultaneously cornering/braking?
parameterization using drum tests
vehicle model for driving simulator
pure handlig with bicycle model?
temperature dependency
vehicle model for motor sports
???
???
mildly uneven roads
vehicle model for ride comfort
MF-Tyre
Magic Formula
Tyre Model
in Different Versions
TMeasy
Tyre Model 'Easy-To-Use'
TameTire
Thermo-Mechanical
Slip-Based
Steady-State
Tire Model (Michelin)
MF-Swift
Short Wavelength
Intermediate Frequency
Tire Model

## Slide 8
CDTire
Comfort
and Durability
Tire Model
Explicit FE
Models
Abaqus,..
RMOD-K 7
Reifenmodell
Komfort
FTire
Flexible
Structure
Tire Model
The Analytic Approach
the analytic approach: ‘focus on cause rather than on effect’
physical, consistent, and comprehensive description of relevant mechanics/thermodynamics/tribology
model-inherent interaction effects between components and features; no need for extra modeling

## Slide 9
The Analytic Approach
CDTire
Comfort
and Durability
Tire Model
Explicit FE
Models
Abaqus,..
RMOD-K 7
Reifenmodell
Komfort
FTire
Flexible
Structure
Tire Model
Tire model (in parts) is teacher:
even the developer can learn from the model’s predicted behavior in new operating points
‘you get more insight than you have programmed’

## Slide 10
The Analytic Approach
CDTire
Comfort
and Durability
Tire Model
Explicit FE
Models
Abaqus,..
RMOD-K 7
Reifenmodell
Komfort
FTire
Flexible
Structure
Tire Model
discretization
abstractions
simplifications
negligances
but yet observing all relevant physical principles

## Slide 11
Why is FTire a teacher?
What can FTire teach us?
How does FTire teach?
FTire and Puzzling Tire Physics: Teacher, not Student

## Slide 12
A lot.
FTire and Puzzling Tire Physics: Teacher, not Student
Some examples:
parking torque
handling on flat road
relaxation length
‘attracting’ cleat
handling on rough road

## Slide 13
tire deformation and stick-slip
when parking at very high wheel load (10 kN)
What can FTire teach us?
Example 1 Parking Torque

## Slide 14
What can FTire teach us?
Example 1 Parking Torque
parking torque depending on inflation pressure and tread depth
inflation pressure
decreasing
tread depth

## Slide 15
What can FTire teach us?
Example 2 Handling on Flat Road
handling characteristics at different tread depths on flat road
decreasing
tread depth
decreasing
tread depth

## Slide 16
What can FTire teach us?
Example 2 Handling on Flat Road
handling characteristics at different inflation pressures on flat road
inflation pressure
inflation pressure

## Slide 17
side force relaxation due to suspension/road induced wheel load ramp up/down
v = 20 km/h, slip angle 6 deg
What can FTire teach us?
Example 3 Relaxation Length

## Slide 18
What can FTire teach us?
Example 3 Relaxation Length
side force relaxation due to slip angle ramp up/down
v = 20 km/h, Fz = 7.8 KN

## Slide 19
What can FTire teach us?
Example 3 Relaxation Length
side force relaxation due to wheel load ramp up/down
v = 20 km/h, slip angle 4 deg

## Slide 20
short period of attracting (positive) longitudinal force at first cleat contact
What can FTire teach us?
Example 4 Cleat ‘Attracting’ the Tire

## Slide 21
What can FTire teach us?
Example 4 Cleat ‘Attracting’ the Tire

## Slide 22
What can FTire teach us?
Example 4 Cleat ‘Attracting’ the Tire

## Slide 23: ^
contact pressure distribution
passing Belgian block road at 50 km/h
What can FTire teach us?
Example 5 Handling on Rough Road

## Slide 24
handling ’characteristics’, unfiltered, on Belgian block road
v = 20 km/h
What can FTire teach us?
Example 5 Handling on Rough Road

## Slide 25
effective handling characteristics on different ISO road classes and on Belgian block
decreasing road quality
decreasing road quality
What can FTire teach us?
Example 5 Handling on Rough Road

## Slide 26
effective handling characteristics at different speeds on Belgian block
speed
speed
What can FTire teach us?
Example 5 Handling on Rough Road

## Slide 27
effective handling characteristics at different tread depths on Belgian block
decreasing tread depth
decreasing tread depth
What can FTire teach us?
Example 5 Handling on Rough Road

## Slide 28: Agenda
Why is FTire a teacher?
What can FTire teach?
How does FTire teach?

## Slide 29: How does FTire teach? FTire Analysis Tools
scripted plot generation
animations + movies
parameterized tire data file
parameterized simulation script
parameter variation loops
on-line parameter variation
result list
detailed tire state output files: contact forces, structure distortion, tread temperature, tire envelope...
result browser
modal analysis, unloaded
steady-state analysis (rolling)
interactive simulation
modal analysis, loaded
property fingerprint
linearization
virtual test bench
static analysis (standing)
cosin/tiretools

## Slide 30
FTire demo versions, papers,
animations, documentation,
version updates, and more:
www.cosin.eu
..thank you for your attention!
Q & A
FTire and Puzzling Tire Physics:
Teacher, not Student